## Slide 1: Coordinating Level-2 Reflectance Products Across Imaging Spectroscopy Missions
David R. Thompson1, Valentina Boccia2, Luigi Agrimano3, Kevin Alonso2, Urs Niklas Bohn1, Philip G. Brodrick1, Marco Celesti2, Raquel De Los Reyes4, Vito De Pasquale3, Regina Eckert1, Ferran Gascon2, Andreas Hüni5, Ray Kokaly6, Jerome Louis7, Francesca Santoro3, Kurtis Thome8, Philip Townsend9, Michael Werfeli5
1 Jet Propulsion Laboratory, California Institute of Technology
2 European Space Agency
3 Planetek Italia
4 DLR Earth Observation Center
5 University of Zurich
6 United States Geological Survey
7 Telespazio, France
8 NASA Goddard Space Flight Center
9 University of Wisconsin, Madison
Instrument
Atmosphere
Surface
Absorption
Scattering
Reflection
Notes: SBG is good to go and address the next levels of detail. The team has developed have a feasible solution that would deploy state-of-the-art technology that is however, at TRL 6thanks to past NASA investments. The community had reviewed and concurs with the level of performance this system can provide, and is strongly behind the envisioned geophysical products. As you’ll see, some of this system’s deficiencies in revisit can be mitigated by NASA’s leadership in international data harmonization and sharing.

## Slide 2: The challenge
Instrument
Atmosphere
Surface
Absorption
Scattering
Reflection

## Slide 3: The importance of L2a harmonization
L2a is foundational: It is necessary for downstream processing attempting to measure Earth surface properties.
Harmonization is useful for CHIME/SBG-VSWIR: One can improve the sampling frequency by combining data from both missions.
There is no single gold standard solution: There are lots of reasonable options, so we must balance consistency with a need to experiment.
Results can be sensitive to changes: Different modeling assumptions can create differences far in excess of instrument noise.

## Slide 4
4
State vector
Measurement
Forward model

## Slide 5
Estimated state
Measurement
Inversion

## Slide 6: Some guiding principles
Differences in product definition are to be avoided, as they prevent interoperability
Differences in forward modeling and/or inversion approaches are inevitable, and do not prevent interoperability with appropriate uncertainty accounting.

## Slide 7: What do we mean by “surface reflectance?”
Is the reflectance of a virtual surface at ground height oriented parallel to the geoid, or
… a terrain facet relative to a Digital Elevation Model?
Is it the Hemispherical Directional Reflectance Factor defined at the observation geometry, or
… simulated for a different geometry?
Is it Remote Sensing Reflectance (Rrs.)?
What strategy is used for geolocalization?

## Slide 8: Topographic effects
Carmon et al., “Shape from Spectra”, RSE 2023

## Slide 9: Glint removal is key for aquatic observations
Marcel König et al., in review
11/13/24

## Slide 10: Provisional parameters for CHIME and SBG-VSWIR
Parameter | CHIME | SBG-VSWIR
Surface definition | Topography-relative | Topography-relative
Digital Elevation Model | Copernicus DEM* | Copernicus DEM*
Ortho basemap | Sentinel-2 GRI | Sentinel-2 GRI
BRDF Correction Applied | Capability will exist | In higher level (L2B+) products
Radiative Transfer Model | LibRadTran*, ERADIATE* | MODTRAN 6.0*, PCRTM, vSmartMOM, or sRTMNet
Glint model | Gege variant* | Gege variant*
Solar Irradiance Model | TSIS* | TSIS*
Aerosol Parameters | AOD, Angstrom Exponent* | AOD, Angstrom Exponent*
Masks | CEOS ARD & Sentinel-2 list | Water, Cloud, Cloud shadow, cloud adjacency. Snow, vegetation, soil, etc. at L2B+
Table 1: Table of reflectance algorithm parameters. Items in bold affect the definition of the target physical quantity being measured, making them the most important areas for coordination. Asterisks (*) indicate answers still to be confirmed.

## Slide 11: Seed questions
How does your work contribute to improving harmonization? Aligning key product definitions, and to the extent possible forward model assumptions.
What aspect of harmonization can most benefit users? Definitions are critical. Rigorous uncertainty quantification is needed to combine multimission data products in a principled way.
At what level of processing is harmonization most necessary (L1B, L1C, L2A, L2B+, L3/L4)? Lower level products, but L2A may be the most challenging from a practical perspective because of the plurality of approaches and definitions.
What is more important, the harmonization on data formats or the harmonization on information content of the products? Information content is most important, since formatting is relatively easy to change on the user side.

## Slide 12: Backup

## Slide 13: New sunglint & skyglint model
Courtesy Niklas Bohn, Marcel König, and others

## Slide 14
prm20221026t191156_rfl – NIR reflectance @ 801 nm (no glint correction)
prm20221026t191156_rfl – NIR reflectance @ 801 nm (glint correction)
prm20221026t191156_rdn – MODIS OC3M Chl-a ()

## Slide 15: Impact of topography on snow observations
Bohn et al., in review

## Slide 16: Retrieval of topography parameters
Carmon et al., RSE 2023
Lidar DSM
Lidar DEM
NASA DEM
Radiance-derived

## Slide 17: Topography aware snow retrievals
Bohn et al., in review