## Slide 1: Japanese spaceborne hyperspectral sensor constellation project
Takahiro Kawashima1, Akira Iwasaki1,
Takayoshi Fukuyo2, Ryo Suzumoto2, Ryo Ui2,
Keita Ito3, Takashi Sukegawa4, Haosheng Lin5, Hirofumi Kasahara6
1The University of Tokyo,
2ArkEdge Space Inc., 3Space BD Inc.,
4CANON Inc., 5HI-Spectral LLC, 6MUFG Bank Ltd.

## Slide 2
Overview
The Small Hyperspectral Sensor Satellite Project is being newly developed under the Small Business Innovation Research (SBIR) program, led by Japanese Ministry of Economy, Trade, and Industry (METI) and scheduled for launch in 2027
While the observation specifications are similar to those of the ISS-borne HISUI, it aims to reduce both mass and cost to about 1/10th of the HISUI.
2
  Mission
  Requirement
System optimization
  Miniaturization
  Heritage of conventional sensors
New technology
HISUI
https://www.hisui.go.jp/sensors/index.html
Type | Hyperspectral sensor (grating type)
Scan method | Push-broom scan
Wavelength region | 400 - 2500 nm
Spectral sampling | 10 nm
GSD | 30m
Swath | 19km
SNR | ~250
Size and mass (allocated for payload) | 200 x 200 x400mm (12U), 20~25kg
SBIR
Small sat
Vegetation
Mineral
Green-house gas
Monolithic spectrograph
eSWIR detector
<Main Specification>

## Slide 3
SBIR sat ( 2027)
～25kg (instrument
only)
~100kg (Bus +
Panchromatic
senor)
HISUI (2019)
190kg (instrument
only)
*Borne on ISS
Custom-made detectors for VNIR&SWIR each Pixel pitch : 30μm
Commercial detector
(VNIR/SWIR integrated)
Pixel pitch : 15μm
Satellite
Spectrometer
Detector
Signal processor
Scanning
method
Telescope
Target
Aperture:
300mm
HgCdTe for SWIR
(120K)
※sample image
HgCdTe for SWIR
(180K)
⇒miniature cooler
※sample image
Miniaturization from HISUI to SBIR hyperspectral sensor
Wavelength region:
400 - 2500nm
Spectral sampling :
10nm (VNIR), 12.5nm (SWIR)
Wavelength region:
400- 2500nm
Spectral sampling:
10nm
Agriculture
Vegetation
etc..
2 spectrometers
1 spectrometer
Monolithic&
Demagnification
optics
3
https://www.hisui.go.jp/sensors/index.html
Mineral
Coast
*Additional for data reduction
Cloud removal
Data compression
Binning
Radiometric correction
Smile correction
Swath
=19 km
DET
Slit
Telescope
SPG
Along Track
Cross Track
GSD=30m
Swath
=20 km
DET
Slit
Telescope
SPG
Along Track
Cross Track
GSD=30m
Green
House gas
Aperture:
170mm

## Slide 4
Engineering and flight models will be manufactured over the next two years.
To shorten the development term, an EFM method, i.e. an EM compatible with the FM, will be manufactured, tested and evaluated, and then refurbished into the FM.
An end-to-end simulator is developed, and correlation with hardware to increase the accuracy of performance simulation, accelerate design evaluation, and reduce rework due to defects to realize short term delivery of a total of two years.
Development plan
4